## Slide 2: Housing
2
Provides for welfare
Keeps the horse safe and healthy; as well as the horse’s handlers
Is cost-effective

## Slide 3: Getting Started
3
Make sure to select a site with the following
  approved for housing livestock animals
  adequate drainage for water and manure
  easily accessible facilities and utilities
    select a site which can be easily reached from a driveway or road
    barn needs to be close to exercise areas
    water and electricity are essential

## Slide 4: Zoning
4
Determine if building codes, construction restrictions or health regulations will prohibit or restrict construction
Regulations exist to protect the quality of life and health of neighbors
Check with local health board for regulations
Check for deed restrictions, easements or rights-of-way upon the property
Always consult with neighbors before building

## Slide 5: Drainage
5
Single most important factor in selecting a location
Needs to provide good drainage away from the building
Ideally, land should slope in all directions
Avoid drainage toward neighbor’s property

## Slide 6: Considerations
6
Purpose of housing
How many and what breed of horses will be housed
Regulatory requirements
Budget
Layout

## Slide 7: Positions & Floors
7
Position stables away from dust sources
Avoid steep slopes to prevent slipping and injuries
Make flooring absorbent, easy to clean and resistant to pawning and slipping
Remove top soil before building stall floors

## Slide 8: Types of Stall Floors
8
Concrete/asphalt
Clay/sand mixture
Limestone/dust
Rubber floor mats
Clay
Wooden floors
Sand

## Slide 9: Door Design
9
Small doorways increase the risk of injury
Sliding doors are very useful
Half-open hinged doors tend to block or decrease the available width of passage
Door should be at least 4’ wide and solidly built
Door latch should be operable from both inside and outside the stall
Door latch should be simple to use, but not simple enough for a smart horse

## Slide 10: Stall Design
10
Should be built of durable, solid materials which will withstand rubbing and kicking of horses
Wood is the most widely used
At least 2” thick wood planking needed
Treated wood recommended for bottom planking
Wood is cheap, but a fire hazard
Walls should be smooth with no protrusions
Can also be made of concrete block or brick
Block and brick is warmer and not a fire hazard
Steel and aluminum can also be used

## Slide 11: Stall Size
11
Depends on the breed of horse and how active the horse is
Ceiling should be no less than 8’

## Slide 12: Ventilation
12
Reduces problems with odor, bacteria and wetness
Circulates air in to keep animals cool in hot summer months
Properly placed and adequately sized vents and roof ducting are essential for ventilation

## Slide 13: Stall Warmth
13
Horses can tolerate a wide range of temperatures
Newborn foals or young stock can be stressed by cold and an extra source of heat may be necessary
Supplemental heating is often used to prevent freezing of water pipes
Drafts should be avoided during extremely cold weather

## Slide 14: Insulation
14
Insulation only keeps stables a few degrees warmer than outside temperature
Insulation decreases the risk of condensation

## Slide 15: Lighting Needs
15
Dark boxes often lead to behavioral problems
Sunlight has ultra-violet light, a natural killer of airborne bacteria and viruses
Approximately 10 percent of skylight in roof is suitable
Light is the main factor in the shedding of hair
Light also stimulates the glands and the production of hormones in the estrous cycle

## Slide 16: Storage Facilities
16
Dust and water in feed areas can lead to forage mites which
  damage feed
  cause skin problems
  cause upset stomachs
Fans or air filters are essential
Storage facilities should be vermin proof and clean

## Slide 17: Water
17
Must be adequate and easily accessible to horse
Via a frost-free hydrant, hose or bucket are least costly methods
Must be kept from freezing in cold weather
Bucket should be emptied, cleaned and refilled daily with fresh water
Via automatic waterers
  saves labor, but is very expensive
  should be checked daily and cleaned with disinfectant regularly

## Slide 18: Fencing
18
Keeps out unwanted animals
Needs to be properly constructed and maintained

## Slide 19: Fencing Considerations
19
Safety
Efficiency
Cost
Aesthetics
Height

## Slide 20: Fencing Materials
20
Wood
  traditional
  sturdy
  expensive, but practical
  requires maintenance
  posts need to be at least 4” squares in diameter

## Slide 21: Fencing Materials
21
Synthetic post and rail fencing
  expensive to install and maintain
  does not require paint

## Slide 22: Fencing Materials
22
Wire fencing
  with a close weave prevents feet from being caught
  is strong and somewhat flexible
Electric fencing
  attached as a single wire on top of a wooden or wire fence
  is not very visible

## Slide 23: Fencing Materials
23
Barbed wire fencing
  is not recommended for horses
  is likely to cause young horses to injure themselves
PVC posts and rails
  are low maintenance
  are cost effective
  are strong and flexible